## Slide 1: RIGOL – Introduction to Radio Frequency Signals
Understanding Time Domain and RF signals
Notes: Today we will be discussing an introduction to RF Signals. We will experiment with creating, transmitting, receiving, and demodulating basic RF signals with instruments in both the time and frequency domain. Once this lab is completed, you should have a basic understanding of the fundamentals of Radio Frequency transmissions.

## Slide 2: What we will learn in this lab section
Viewing basic RF signals in the time and frequency domain
Converting amplitude to power
Basic Modulation Schemes
Transmitting analog data
  Analog Modulation
  Analog Demodulation
Transmitting digital data
  Simple Digital Modulation
  Simple Digital Demodulation
Complex digital modulation schemes
Notes: There are several steps in RF signal processing and analysis. We will use our benchtop instrumentation to help visualize each step.
The first step is to find the best way to visualize different signals in both RF and time domains.
Since an oscilloscope, which views the time domain, measures amplitude in voltage and a spectrum analyzer measures amplitude in power we will discuss how to convert and compare these values.
Next, we will discuss and visualize several basic modulation schemes.
Once we have a basic understanding of how RF signals can be modulated we will look more closely at some methods of transmitting analog information.
Once we are comfortable with the analog modulation concepts we will see how digital modulation is different. Digital modulations are the foundation of modern RF signals since the vast majority of transmitted data today is digital so that it can be processed and used by computers in one way or another.
Finally, we will take a brief conceptual look at complex modulations like those used in Wifi and bluetooth signals for a comparison to our basic modulations.

## Slide 3: Equipment we will be using in this lab
DG1022Z Waveform Generator
DS1054Z Oscilloscope
DSA705 Spectrum Analyzer
1 mono audio jack to BNC cable
2 BNC cables
1 BNC tee
1 N-type to BNC Converter
2 low frequency antennas (with male BNC connectors or adaptors)
USB stick with setup files that came with this lab
Notes: The instrumentation and cabling we will need is listed here.
The setup files included in this content package were created on instruments with these firmware levels:
DG1022Z with FW level: 00.01.12
DS1054Z with FW level: 00.04.04.SP3
We have created setup files for 4 different Spectrum Analyzer model including:
DSA1030 with FW level: 0.1.1
DSA815 with FW level: 01.19
DSA710 with FW level: 01.19
RSA3030-TG with FW level: 01.01
Some setup files will work on other FW versions and models as well.

## Slide 4: Viewing Signals with our Instruments
Before we get started let’s set up our instruments
Load the start setup files for the generator, analyzer, and oscilloscope
Connect the DG1Z channel 1 output with a BNC tee to the RF input on the analyzer and the channel 1 input on the oscilloscope
Notes: Connect the RF input and the Scope CH1 input to the CH1 output on the DG1000Z using BNC cables, the BNC-Tee, and the BNC to N-type adaptor on the front of the Spectrum Analyzer.
At this point you can also load the Setup files for each instrument to begin viewing the first test signal. These are the “start” setup files in the Start folder.

## Slide 5: The difference between frequency and time domain
In the time domain we view signals on an oscilloscope with time on the X axis
In frequency domain we use a spectrum analyzer with frequency on the X axis
Amplitude or Power is on the Y axis
These 2 domains can be thought of as different views on the same 3 dimensional chart
By Phonical - Own work, CC BY-SA 4.0, https://commons.wikimedia.org/w/index.php?curid=64473578
Time Domain View
Frequency Domain View
Notes: This is one way to think about the difference between the time and frequency domains. The Oscilloscope shows you the view on the left with time on the X axis. The Spectrum Analyzer shows frequency on the X axis. For RF signals both are important attributes of a signal. In discussing the first few basic types of modulation we will see how many of them are easier to visualize and understand in the frequency domain, but some can only be understood with time domain information.

## Slide 6: Viewing RF signals in the time domain
We view signals in the time domain with an Oscilloscope
A simple sine wave with only one frequency is called a RF Carrier
Here is a 10 MHz carrier shown on our Oscilloscope
The scope shows time on the X axis and voltage on the Y axis
The red oval shows the frequency measurement
The blue oval and line shows the time between horizontal divisions
The period of each wave is 100 ns. These numbers match since 1/period = frequency
Vpp (Voltage peak to peak) is how far the signals moves in voltage (shown with orange oval and line)
Notes: Basic view of a 10 MHz sine wave on the oscilloscope with explanation about basic measurements and characteristics.

## Slide 7: Viewing the same signal in the Frequency domain
We view signals in the frequency domain with a Spectrum Analyzer
A carrier looks very simple in this view
An Analyzer shows frequency on the X axis and Power on the Y axis
Most analyzers like this one have a 50 Ohm input
Analyzers measure Power in dBm
dBm is a log unit of power where:
  10 dBm = 10 mWatt
  0 dBm = 1 mWatt
  -10 dBm = 100 µWatt
  -20 dBm = 10 µWatt and so on
The red oval shows the frequency measurement at the peak
Notes: Basic view of a 10 MHz sine wave on the Spectrum Analyzer with explanation about basic measurements and characteristics.

## Slide 8: Converting amplitude to power
Power in dBm = 10 log10(Vrms2/R) + 30
R = 50 Ohm
For a clean Sine wave Vrms = Vpp*~0.707
Therefore 1 Watt = 30 dBm = 10*log10(1)+ 30
We add 30 because 0 dBm = 1 mW instead of 1 Watt
Vrms2/R = 1 when Vrms = √50 = ~7.071
So, 1 Watt is produced by 20 Vpp or 7.071 Vrms into 50 Ohms
Our signal is ~-25 dBm which is equal to about 11 mVrms. In these ranges the Spectrum Analyzer is much more precise than the scope
Notes: Process for converting amplitude between power and voltage.

## Slide 9: Amplitude modulation
Modulation is the encoding of information on a carrier for transmission. The most basic method is amplitude modulation like an AM radio station
AM varies the power or amplitude over time
Oscilloscope Spectrum Analyzer
Notes: AM stands for Amplitude Modulation. Amplitude modulation alters the power and voltage over time. On the scope this appears as overlapping sine waves of different sizes. The amplitude is changing quickly here. The Spectrum Analyzer shows the peak at 10 MHz moving up and down. This appears to be moving more slowly because as the instrument sweeps it catches different power levels in this frequency as it passes and they are then displayed on the screen. It is worth noting that this type of modulation does not emit significant power into the adjacent spectrum. However, amplitude is very susceptible to range especially when being transmitted wirelessly over distance. This is one reason why AM radio stations tend to have poorer sound quality than FM stations since obstacles will lessen the received amplitude and eventually impact the dynamic range.
The setup file for the DG1Z is in the AM folder. All other instruments use the same start settings.

## Slide 10: Frequency modulation
Frequency Modulation changes the frequency to transmit information
FM varies the frequency over time
On the Oscilloscope, the time On the Analyzer, the power appears
between sine peaks is changing across multiple frequencies
Notes: Frequency Modulation is shown on the oscilloscope as a sine wave with varying time between peaks. This signal varies around the 10 MHz carrier. On the Spectrum Analyzer we can clearly see the minimum and maximum frequencies between which the signal is moving. Both of these views also show the analog nature of this signal. We can see that the actual frequency at any time may be one of many frequency values between the lowest and highest values.
The setup files for the instruments are in the FM folder.

## Slide 11: Phase modulation
Phase Modulation changes the Phase of a signal to transmit information
The relative phase changes over time
On the scope, we can see the Sine On the Analyzer, the phase changes
wave change its phase by 180° create harmonics in many frequencies
Notes: Phase Modulation is our third type of modulation. To make this easier to visualize we are using a more digital type of modulation. This is a type called Phase Shift Key or PSK modulation. Here we have programmed the generator to quickly change the phase from 0 degrees to 180 degrees thousands of times per second. On the scope we are capturing the event where the phase changes abruptly. You can see where the signal enters the display with the positive portion of the sine wave first. It then leaves the display on the right going in the negative direction. This display is set to 50 ns/div which equals 600 ns across the display. The 10 MHz sine wave should have exactly 6 cycles on the screen. Since it enters crossing zero in the positive direction and leaves going negative we can see that the phase has changed by 180 degrees.
The effect of this abrupt change creates an interesting spectrum on the analyzer as well. We can see that unwanted signals are being generated in the adjacent bandwidth. The wave does not strictly contain full cycles of sine waves at those other frequencies, but the power in the abrupt phase change is spread out across the spectrum in this manner. The faster the modulation and usually the more abrupt change the more spurious signal is generated. This is an important aspect of RF signals since they all exist in a shared spectrum. Interference between signals and channels is a constant challenge for designers of transmission protocols.
The setup files for the DG1Z and DS1Z are in the AM folder. Analyzers use the same start settings.

## Slide 12: Transmitting Analog Data
Both AM and FM are easy to use for analog data because you can set multiple set points of amplitude or frequency to encode the analog signal
AM Experiment: connect a audio source (phone) to the DG1Z’s CH1 ext mod input
Load the AM Tx setup files
Connect headphones or earbuds to the DSA jack
Listen to the audio transmitted via the cable
Switch the DG1Z and DSA to antennas. Static comes from amplitude distortion from the wireless transmission
Notes: Now lets look at a real life example of an analog data transmission.
Here we will transmit audio using Amplitude modulation.
This experiment uses just one audio channel (right or left) so use or create a mono jack to BNC. Connect the audio track source to the center pin of the CH 1 Modulation input in the back of the DG1Z. The ground should be connected to the shield of the BNC.
For both of these experiments you will need to adjust the volume of the audio, the gain and volume of the demod settings on the analyzer. You may also need to adjust the power of the Carrier on the DG1Z when using the antennas in order to get a clear signal.
The setup files for the DG1Z and Spectrum Analyzer are in the “AM external” folder. From there you can make gain and volume adjustments.

## Slide 13: Transmitting Analog Data
FM Experiment
Leave the connections
Load the FM Tx setup files
Listen to the audio transmitted via the cable and the antennas
Frequency is less effected by environmental changes such as range and interference. Once the amplitude is high enough and the deviation set correctly this signal should be clearer than the AM signal
The impact of interference and range is a main reason why FM radio stations tend to be clearer than AM radio stations
Notes: This experiment does the same thing except with Frequency modulation.
In general it should be easier to adjust the settings to get a clean FM signal especially if you are using the antennas.
It should also be noted how much easier it is to view the variations due to these modulations on the analyzer than the Oscilloscope. That is especially true for FM modulation when using relatively small frequency changes to encode that data.
For this experiment you will need to adjust the volume of the audio, the gain and volume of the demod settings on the analyzer. You may also need to adjust the power of the Carrier on the DG1Z when using the antennas in order to get a clear signal.
The setup files for the DG1Z and Spectrum Analyzer are in the “FM external” folder. From there you can make gain and volume adjustments.

## Slide 14: Transmitting Digital Data
Amplitude & Frequency modulations can also be used to carry digital data
We call these ASK and FSK for amp or freq “shift key”
In these modulations, there are just 2 levels of amplitude or 2 frequencies
One is demodulated as a binary ZERO, the other a binary 1
Connect the DSA demod jack to scope channel 2 and load the ASK setups
Note the modulation shifts at 1 ms increments – 1 division on each
Notes: Load the setup files in the ASK folder

## Slide 15: Transmitting Digital Data
Now load the FSK setup
This shifts the frequency from two close values (9.9 and 10 MHz)
The change can not be easily seen on the scope, but the demodulation is very clean
Notes: Load the setup files in the FSK folder

## Slide 16: Efficient use of spectrum
One key advantage to advanced modulation schemes is that they use spectrum much more efficiently
Much like our FSK signal that stayed within a narrow frequency range, modulations are optimized so that many signals can be sent along side each other in ‘channels’
This is frequency division multiplexing or dividing the usable spectrum into frequency channels
Advanced signals may also use other types of multiplexing including time or phase to transmit more data in the available spectrum

## Slide 17: Complex signals for WiFi usage
A more complex modulation seen in some WiFi signals would be QAM
Quadrature Amplitude Modulation
There are 2 sine waves at the same frequency but are 90° out of phase
We call these signals I and Q
Each of the 2 waves is modulated with a ASK and PSK signal
Basic QAM16 is a demodulation with 16 possible values shown here
This is called a ‘Constellation diagram’
By Chris Watts - Own work, CC BY-SA 3.0, https://commons.wikimedia.org/w/index.php?curid=15781908
See how the bit values are determined by both the relative amplitude and phase of the signals

## Slide 18: More advanced instrumentation
RF Design engineers utilize sophisticated instruments to design, test, and verify complex modulations
Many RF transmission strategies are derived from these basic principles while trying to:
decrease power to save battery life
improve signal to noise ratio to reduce errors
be more efficient with bandwidth to improve density

## Slide 19: Monitoring the relationship between 2 signals with a scope
For this experiment, connect the 2 channels of the generator directly to channels 1 and 2 on the oscilloscope
First, load the XY_ask setup file for the scope
Then, load the ASK setup files for the generator and view the signal
Finally, load the PSK setup file for the generator and the XY_psk setup file for the scope and view the signal

## Slide 20: Demonstrating ASK and PSK modulation with 2 signals
View the pattern of 2 ASK signals that are constantly at a 90° phase offset and the same frequency
Note the 2 levels of the ASK: one is 25% of the other
Note that the 2 signals are never stay at the same or opposite level since they 90° out of phase
The PSK signal stays always at the same or opposite level since it changes from the identical wave to inverted.
XY mode is useful for visualizing signal relationships
180° PSK signals at 90 degrees
2 ASK signals 90° out of phase
Notes: After loading the DG1Zqam setup file turn both outputs on. Then set the start phase of CH1 until the scope looks like the image on the top.
This is when they are 90 degrees out of phase. You can also use the phase difference measurement to approximate this.
Because they are 90 degrees out of phase when one signal is at a max or min value the other is at a zero crossing. The combination of these and the 2 different amplitude levels makes the figure on the X-Y chart.
The Lissajous or XY curves visually demonstrate the phase offset between the 2 channels. When the phase is 90 or 270 degrees the figures are circular. We therefore can adjust the phase offset to make the figures circular and that indicates the 2 sinusoids are at a 90 degree offset.

## Slide 21: Summary
RF signals transmit data by changing frequency, amplitude, and phase over time
These can be combined into complex, efficient modulation schemes
Analog modulations can transmit complex signals like audio
Digital modulations transmit binary data which is used in virtually all computer and electronic systems – WiFi, Bluetooth, and Cellular are different types of digitally modulated signals for different purposes
Being able to think about signals in frequency or time domain is beneficial to engineers in a variety of fields